## Slide 1: Smart Agriculture: Crop and Plant Health Monitoring and Air Quality Monitoring System using Arduino UNO
Capstone Project | SE / Semester III | Team ID: ____
Student Name 1 (Roll No. ____) Student Name 2 (Roll No. ____)
Student Name 3 (Roll No. ____) Student Name 4 (Roll No. ____)
Department of Computer Engineering
Faculty Guide: Megha Godboley, Assistant Professor, Computer Department, SJCEM
St. John College of Engineering & Management, University of Mumbai
Academic Year: 20____ - 20____
Notes: Introduce the project title, team members, guide and institution.

## Slide 2: Problem Statement & Motivation
THE PROBLEM
Soil dryness, air temperature, humidity and air quality around plants are still judged by eye or by touch on small farms, nurseries and gardens.
Manual checking gives no numeric value and changes from person to person. Commercial monitoring kits exist, but they are costly and built for large installations.
PROPOSED SOLUTION
A battery-powered Arduino UNO unit that reads soil moisture, temperature, humidity and air quality and shows them live on a 16x2 LCD.
WHY MANUAL CHECKING FALLS SHORT
0
numeric readings from touch-and-look checking
4
parameters shown together by one low-cost unit
Notes: The gap: no numeric, repeatable readings on small farms. Our unit shows four parameters on-site without a phone or internet.

## Slide 3: Project Objectives & Scope
Primary objective
Technical targets
Boundaries / out of scope
Build a working prototype that continuously measures the soil and air conditions important for crop and plant health and shows them on a local display.
Keep it portable, battery powered and built from commonly available parts.
4
parameters: soil moisture, temperature, humidity, air quality
3
sensors read by one Arduino UNO
16x2
LCD shows all live readings
9 V + 3.7 V
battery supply, no mains needed
No wireless or cloud connectivity
No data logging or alerts
No automatic irrigation
Single sensing point; bench and small-scale plant tests only
Sensor accuracy limited to the low-cost parts used
Notes: Primary objective, the measurable targets of the prototype, and what is explicitly out of scope for a second-year timeline.

## Slide 4: Literature Survey & Gap Analysis
Prior work | What it does | Cost | Latency | Modularity | Cloud access
Giacobbe et al., Univ. of Messina: IoT + AI plant health and pathogen detection | Growth-data sensing with AI at the edge, shown for tomato crops | Higher: specialised phenotyping sensors | Edge processing | Crop-specific | IoT-connected
Plant Monitoring System using KNN (EasyChair Preprint 9698, 2023) | IoT + machine learning; soil moisture, DHT11 and level sensors | Low to medium | Network-dependent | Multi-sensor | IoT-based
Crop monitoring and smart farming using IoT (GeeksforGeeks) | Arduino Uno with soil, DHT22, MQ gas sensors, LCD and SMS alerts | Low | SMS-based alerts | Many sensors | SMS / remote
Our project | Arduino UNO with soil, DHT11, MQ135 and LCD in one box | Low | Instant, on-device | Sensors can be added | None (fully offline)
Gap: existing work either depends on connectivity or AI, or adds alerts through extra modules. Our project targets the simplest case: a low-cost, offline unit that shows all readings at a glance. Alerts and connectivity are the next step.
Notes: Three prior works compared on cost, latency, modularity and cloud access. Ratings are qualitative and based on the description of each work.

## Slide 5: Proposed System Architecture
DHT11
temperature + humidity
MQ135
air quality
Soil moisture sensor
soil dryness / wetness
digital (pin 7)
analog
analog
Power: 9 V + 3.7 V cells, switch
Arduino UNO
ATmega328P
reads sensors, converts ADC values, formats output
16x2 LCD display
live readings for the user
10k preset: LCD contrast adjustment
DATA FLOW, LAYER BY LAYER
1
Sensing
Sensors convert soil moisture, gas level, temperature and humidity into signals
2
Acquisition
Analog outputs pass through the 10-bit ADC (0 to 1023); DHT11 sends digital data
3
Processing
The sketch reads each value and prepares text for the display
4
Output
The LCD shows the readings and refreshes as conditions change
Notes: Input: three sensors. Processing: Arduino UNO. Output: 16x2 LCD. Power comes from a 9 V battery with a 3.7 V cell in series.

## Slide 6: ER Diagram & Database Schema
SENSOR_NODE
node_id (PK)
location
crop_type
READING
reading_id (PK)
node_id (FK)
recorded_at
temperature_c
humidity_pct
air_quality_raw
soil_moisture_raw
has
1
N
One node (a monitoring unit) records many readings over time. Each reading holds the four measured values.
Table | Column | Type | Key
sensor_node | node_id | INT | PK
 | location | VARCHAR(50) | 
 | crop_type | VARCHAR(30) | 
reading | reading_id | INT | PK
 | node_id | INT | FK
 | recorded_at | DATETIME | 
 | temperature_c | FLOAT | 
 | humidity_pct | FLOAT | 
 | air_quality_raw | INT | 
 | soil_moisture_raw | INT | 
Note: the current prototype is a standalone unit and stores no data. This schema is the planned data-logging extension (future scope), with one reading saved per sensor cycle.
Notes: The prototype has no database. The ER diagram and schema show how readings would be stored when logging is added.

## Slide 7: Tech Stack & Methodology
Hardware
Arduino UNO (ATmega328P) as controller
DHT11 (single-wire digital, pin 7), MQ135 and soil moisture sensor (analog)
16x2 LCD with 10k contrast preset
9 V battery + 3.7 V rechargeable cell, switch, enclosure
No I2C, SPI, UART or CAN used
Software & tools
Arduino IDE to write and upload the sketch
Arduino C/C++ language
DHT sensor and LiquidCrystal libraries
ADC: 10-bit, values 0 to 1023
No cloud, database or ML in the prototype
EXECUTION WORKFLOW
1
Select & prepare
Choose sensors; solder LCD wires; add contrast preset
2
Assemble
Mount parts in the box; jumper wiring; extend the soil probe wire
3
Firmware
Write and upload the sketch: read sensors, print on LCD
4
Integrate & test
Add 9 V + 3.7 V supply; test dry / wet soil, open / closed box, near plants
Notes: Hardware and software used, followed by the four phases of the build.

## Slide 8: Hardware Prototype / Experimental Setup
Prototype photograph
Insert the photo of the assembled unit here, then place markers 1 to 6 on the components
KEY CALLOUTS
1
Power circuit
9 V battery, 3.7 V cell, switch, power jack
2
MCU board
Arduino UNO
3
Display
16x2 LCD with contrast preset
4
Air-quality sensor
MQ135, exposed through box openings
5
Temp / humidity sensor
DHT11
6
Soil probe
Soil moisture sensor on extended wire
Tested: dry soil vs water, enclosure open vs closed, unit near plants
Notes: Show the assembled prototype and point out each numbered component.

## Slide 9: Team Division of Work
1
Circuit & Hardware
Student Name 1 (Roll No. ____)
Wiring of sensors, Arduino and LCD
LCD soldering and contrast preset
Battery supply and enclosure
2
Firmware & Sensor Interfacing
Student Name 2 (Roll No. ____)
Arduino sketch and libraries
Reading DHT11, MQ135, soil sensor
LCD output formatting
3
Testing & Calibration
Student Name 3 (Roll No. ____)
Dry / wet soil test
Open / closed enclosure test
Field test near plants
4
Documentation & Presentation
Student Name 4 (Roll No. ____)
Project report and references
Presentation and demo video
Component list and diagrams
Notes: Each member owned one area. Replace the placeholder names and roll numbers with the real ones.

## Slide 10: Conclusion & Future Scope
Summary: objectives met
Built a standalone unit that measures soil moisture, temperature, humidity and air quality.
All four readings appear live on a 16x2 LCD.
Battery powered and housed in a box with openings for airflow.
Readings responded correctly to dry and wet soil, open and closed enclosure, and placement near plants.
Future work (3rd / 4th year)
Connectivity: ESP32 with a cloud dashboard or mobile app
Data logging: store readings using the planned schema
Alerts: buzzer or SMS when a limit is crossed
Automation: relay and pump for automatic irrigation
Hardware: custom PCB and weatherproof enclosure
Intelligence: ML for plant health or disease prediction
Notes: Recap that the objectives were fulfilled and outline how the project can grow in later years.